## Slide 1: INTRO TO EMBEDDED SYSTEMS WORKSHOP
Tsen Chee Vincent LEUNG YIN KO

## Slide 2: AGENDA
Introduction to Embedded Systems
Hands on Workshop!
Hardware familiarization
Software familiarization
Actuators and Sensors
Demo of applications

## Slide 3: WHAT ARE EMBEDDED SYSTEMS
WHAT IS IT
“Dumb” Devices
Smart Devices
Internet of Things
Robotics
WHERE IS IT
Anything “Smart”
Microwaves/Fridges
Drones/Self Driving Cars
NASA Rovers
Biochips

## Slide 4: PROVIDED SUPPLIES
ARDUINO UNO/MEGA (1x)
USB CABLE (1x)
BREADBOARD (1x)
HOOKUP WIRE (1m Black, 1m Red)
LED (5x)
BUTTONS (2x)
RESISTORS (7x 330Ω, 2x 1kΩ)
CAPACITORS (2x 33nF, 2x 100nF, 2x 470μF)

## Slide 5: ACTIVITY 1 SETUP THE BRAIN
Task: Write “Hello World” on the Serial Monitor
Outcome
Microcontroller documentation
Arduino IDE Setup
Hardware + Software familiarization
Overview
☐ Arduino Datasheet
☐ Connection
☐ Arduino IDE Installation
☐ “Hello World”
☐ Flashing
☐ Serial Monitor
Hardware

## Slide 6
Overview
☐ Arduino Datasheet
☐ Connection
☐ Arduino IDE Installation
☐ “Hello World”
☐ Flashing
☐ Serial Monitor
ACTIVITY 1 SETUP THE BRAIN
Download the Arduino Datasheet (https://docs.arduino.cc/hardware/uno-rev3)
Hardware

## Slide 7
Overview
☐ Arduino Datasheet
☐ Connection
☐ Arduino IDE Installation
☐ “Hello World”
☐ Flashing
☐ Serial Monitor
ACTIVITY 1 SETUP THE BRAIN
Download the Arduino Datasheet (https://docs.arduino.cc/hardware/uno-rev3)
Hardware
1
2
3
4

## Slide 8: ACTIVITY 1 SETUP THE BRAIN
Connect Arduino to PC via USB Cable
Overview
☑ Arduino Datasheet
☐ Connection
☐ Arduino IDE Installation
☐ “Hello World”
☐ Flashing
☐ Serial Monitor
Hardware

## Slide 9
Download the Arduino IDE v2.x (https://docs.arduino.cc/software/ide-v2)
Install & Launch
Overview
☑ Arduino Datasheet
☑ Connection
☐ Arduino IDE Installation
☐ “Hello World”
☐ Flashing
☐ Serial Monitor
ACTIVITY 1 SETUP THE BRAIN
Hardware

## Slide 10
Overview
☑ Arduino Datasheet
☑ Connection
☑ Arduino IDE Installation
☐ “Hello World”
☐ Flashing
☐ Serial Monitor
ACTIVITY 1 SETUP THE BRAIN
Code a simple “Hello World”
Hardware

## Slide 11
Overview
☑ Arduino Datasheet
☑ Connection
☑ Arduino IDE Installation
☑ “Hello World”
☐ Flashing
☐ Serial Monitor
ACTIVITY 1 SETUP THE BRAIN
Tools -> Board -> Arduino AVR Boards -> Arduino Uno
1
2
3
4
Hardware

## Slide 12
Overview
☑ Arduino Datasheet
☑ Connection
☑ Arduino IDE Installation
☑ “Hello World”
☐ Flashing
☐ Serial Monitor
ACTIVITY 1 SETUP THE BRAIN
Tools -> Port -> COM[X]
1
2
3
Hardware

## Slide 13
Overview
☑ Arduino Datasheet
☑ Connection
☑ Arduino IDE Installation
☑ “Hello World”
☐ Flashing
☐ Serial Monitor
ACTIVITY 1 SETUP THE BRAIN
Board “Arduino Uno”, Port “COM[X]”
Winning?
Hardware

## Slide 14
Overview
☑ Arduino Datasheet
☑ Connection
☑ Arduino IDE Installation
☑ “Hello World”
☐ Flashing
☐ Serial Monitor
ACTIVITY 1 SETUP THE BRAIN
Flash -> Upload Files (Aka“Flashing”)
1
2
Hardware

## Slide 15
Overview
☑ Arduino Datasheet
☑ Connection
☑ Arduino IDE Installation
☑ “Hello World”
☐ Flashing
☐ Serial Monitor
ACTIVITY 1 SETUP THE BRAIN
Notice output console magicks + details
Hardware

## Slide 16
Overview
☑ Arduino Datasheet
☑ Connection
☑ Arduino IDE Installation
☑ “Hello World”
☑ Flashing
☐ Serial Monitor
ACTIVITY 1 SETUP THE BRAIN
Tools -> Serial Monitor
What do you see?
1
2
Hardware

## Slide 17
Overview
☑ Arduino Datasheet
☑ Connection
☑ Arduino IDE Installation
☑ “Hello World”
☑ Flashing
☐ Serial Monitor
ACTIVITY 1 SETUP THE BRAIN
Tools -> Serial Monitor
What do you see? Hello World!
Hardware

## Slide 18: ACTIVITY 1 SETUP THE BRAIN
Task: Write “Hello World” on the Serial Monitor
Outcome
Microcontroller documentation
Arduino IDE Setup
Hardware + Software familiarization
Recap
Arduino is a Microcontroller/the Brains
Programmable - “Flashable”
Can communicate
Overview
☑ Arduino Datasheet
☑ Connection
☑ Arduino IDE Installation
☑ “Hello World”
☑ Flashing
☑ Serial Monitor
Hardware

## Slide 19: ACTIVITY 2 BLINK FOR HELP
Task: Blink the built-in LED to morse code (SOS)
Outcome
Microcontroller documentation
Hardware + Software familiarization
Output / Actuator intro
Hardware
Overview
☐ Input and Output
☐ Analog/Digital GPIO
☐ Turn ON/OFF Built-in LED
☐ Blink SOS
☐ Physical Limitations (Datasheets!)

## Slide 20: BREAK TIME RESUME AT:

## Slide 21: ACTIVITY 2 BLINK FOR HELP
Task: Blink the built-in LED to morse code (SOS)
Outcome
Microcontroller documentation
Hardware + Software familiarization
Output / Actuator intro
Hardware
Overview
☐ Input and Output
☐ Analog/Digital GPIO
☐ Turn ON/OFF Built-in LED
☐ Blink SOS
☐ Physical Limitations (Datasheets!)

## Slide 22
ACTIVITY 2 BLINK FOR HELP
Communication? Input? Output?
Receive? Send?
Overview
☐ Input and Output
☐ Analog/Digital GPIO
☐ Turn ON/OFF Built-in LED
☐ Blink SOS
☐ Physical Limitations (Datasheets!)
Hardware

## Slide 23
ACTIVITY 2 BLINK FOR HELP
General Purpose Input Output (GPIO)
Both Analog GPIO and Digital GPIO
Hardware
Overview
☑ Input and Output
☐ Analog/Digital GPIO
☐ Turn ON/OFF Built-in LED
☐ Blink SOS
☐ Physical Limitations (Datasheets!)

## Slide 24
ACTIVITY 2 BLINK FOR HELP
Turn ON/OFF LED, Use Digital GPIO!
We’ll use “LED_BUILTIN”
Hardware
Overview
☑ Input and Output
☑ Analog/Digital GPIO
☐ Turn ON/OFF Built-in LED
☐ Blink SOS
☐ Physical Limitations (Datasheets!)

## Slide 25
ACTIVITY 2 BLINK FOR HELP
Arduino IDE, File -> New
Set “LED_BUILTIN” to OUTPUT mode!
Turn it OFF and ON
Flash!
Hardware
Overview
☑ Input and Output
☑ Analog/Digital GPIO
☐ Turn ON/OFF Built-in LED
☐ Blink SOS
☐ Physical Limitations (Datasheets!)

## Slide 26
ACTIVITY 2 BLINK FOR HELP
Blink SOS morse code (· · ·---· · ·)
Use functions
Hardware
Overview
☑ Input and Output
☑ Analog/Digital GPIO
☑ Turn ON/OFF Built-in LED
☐ Blink SOS
☐ Physical Limitations (Datasheets!)
Morse Code
Dot 100ms
Dash 300ms
Between Dots and Dashes 100ms
Between Letters 300ms
Between Words 700ms
S · · ·
O ---
S · · ·

## Slide 27
ACTIVITY 2 BLINK FOR HELP
Flash!
Hardware
Morse Code
Dot 100ms
Dash 300ms
Between Dots and Dashes 100ms
Between Letters 300ms
Between Words 700ms
S · · ·
O ---
S · · ·
Overview
☑ Input and Output
☑ Analog/Digital GPIO
☑ Turn ON/OFF Built-in LED
☐ Blink SOS
☐ Physical Limitations (Datasheets!)

## Slide 28
ACTIVITY 2 BLINK FOR HELP
Try reducing the time by a factor of 10x
Reduce it by a factor of 100x
Does it still blink?
Is it still bright?
Hardware
Morse Code
Dot 100ms
Dash 300ms
Between Dots and Dashes 100ms
Between Letters 300ms
Between Words 700ms
S · · ·
O ---
S · · ·
Overview
☑ Input and Output
☑ Analog/Digital GPIO
☑ Turn ON/OFF Built-in LED
☑ Blink SOS
☐ Physical Limitations (Datasheets!)

## Slide 29
ACTIVITY 2 BLINK FOR HELP
Typical LED Datasheet
Further reading: Pulse Width Modulation (PWM)
Hardware
Overview
☑ Input and Output
☑ Analog/Digital GPIO
☑ Turn ON/OFF Built-in LED
☑ Blink SOS
☐ Physical Limitations (Datasheets!)

## Slide 30: ACTIVITY 2 BLINK FOR HELP
Task: Blink the built-in LED to morse code (SOS)
Outcome
Microcontroller documentation
Hardware + Software familiarization
Output / Actuator intro
Recap
A/O GPIO
Knowledge in documentation and/or datasheets!
Know the limitations (software and hardware)
Hardware
Overview
☑ Input and Output
☑ Analog/Digital GPIO
☑ Turn ON/OFF Built-in LED
☑ Blink SOS
☑ Physical Limitations (Datasheets!)

## Slide 31: ACTIVITY 3 LIGHTBRINGER
Task: Blink an external LED to morse code (SOS) on command
Outcome
Schematic reading (basic)
Hardware + Software familiarization
Serial & Serial Monitor
Hardware
Overview
☐ Connect External Hardware
☐ Modify SOS
☐ Send command via Serial

## Slide 32: BREAK TIME RESUME AT:

## Slide 33: WORKING WITH ELECTRONICS
Fundamentals
Power source (AC/DC)
Voltage = Current x Resistance
Ground, Ground, Ground
If in doubt, there’s no doubt, double check & ask
Breadboard?
Build prototypes
Connect using “hookup wire”

## Slide 34: ACTIVITY 3 LIGHTBRINGER
Task: Blink an external LED to morse code (SOS) on command
Outcome
Schematic reading (basic)
Hardware + Software familiarization
Serial & Serial Monitor
Hardware
Overview
☐ Connect External Hardware
☐ Modify SOS
☐ Send command via Serial

## Slide 35
ACTIVITY 3 LIGHTBRINGER
DISCONNECT!
Hardware
Overview
☐ Connect External Hardware
☐ Modify SOS
☐ Send command via Serial
+
-
Flat – Cathode
Long – Anode

## Slide 36
ACTIVITY 3 LIGHTBRINGER
Wire as per schematic
Hardware
Overview
☐ Connect External Hardware
☐ Modify SOS
☐ Send command via Serial
+
-
Flat – Cathode
Long – Anode

## Slide 37
ACTIVITY 3 LIGHTBRINGER
Hardware
Overview
☐ Connect External Hardware
☐ Modify SOS
☐ Send command via Serial
Wiring Check
+
-
Flat – Cathode
Long – Anode

## Slide 38
ACTIVITY 3 LIGHTBRINGER
Modify Activity 2 code (Blink for Help, SOS) to work with digital pin 13
Make a variable “led_pin” and swap it for “LED_BUILTIN” (everywhere, not only `setup()`)
Connect & Flash!
Hardware
Overview
☑ Connect External Hardware
☐ Modify SOS
☐ Send command via Serial

## Slide 39
ACTIVITY 3 LIGHTBRINGER
Hardware
Overview
☑ Connect External Hardware
☐ Modify SOS
☐ Send command via Serial

## Slide 40
ACTIVITY 3 LIGHTBRINGER
Serial Monitor is not a pure monitor!
Use `Serial.readString()`
Hardware
Overview
☑ Connect External Hardware
☑ Modify SOS
☐ Send command via Serial

## Slide 41
ACTIVITY 3 LIGHTBRINGER
Something like this? Flash!
Hardware
Overview
☑ Connect External Hardware
☑ Modify SOS
☐ Send command via Serial

## Slide 42
ACTIVITY 3 LIGHTBRINGER
“Ctrl + Shift + M” to open Serial Monitor
“Ctrl + Enter” to send message
Hardware
Overview
☑ Connect External Hardware
☑ Modify SOS
☐ Send command via Serial

## Slide 43
ACTIVITY 3 LIGHTBRINGER
Note the option to change line endings.
How quickly is your command registered?
What happens if you change the “baud” rate?
Hardware
Overview
☑ Connect External Hardware
☑ Modify SOS
☐ Send command via Serial

## Slide 44: ACTIVITY 3 LIGHTBRINGER
Task: Blink an external LED to morse code (SOS) on command
Outcome
Schematic reading (basic)
Hardware + Software familiarization
Serial & Serial Monitor
Recap
Build your own circuits
Knowledge in documentation and/or datasheets!
Know the limitations (software and hardware)
Hardware
Overview
☑ Connect External Hardware
☑ Modify SOS
☑ Send command via Serial

## Slide 45: ACTIVITY 4 KNIGHT RIDER
Task: Blink LEDs from left to right. Change speed with buttons.
Outcome
Hardware + Software familiarization
Input / Sensor
Hardware
Overview
☐ More LEDs
☐ Buttons (Pull-up config) & Debouncing
☐ Code “Knight Rider” effect

## Slide 46: BREAK TIME RESUME AT:

## Slide 47: ACTIVITY 4 KNIGHT RIDER
Task: Blink LEDs from left to right. Change speed with buttons.
Outcome
Hardware + Software familiarization
Input / Sensor
Hardware
Overview
☐ More LEDs
☐ Buttons (Pull-up config) & Debouncing
☐ Code “Knight Rider” effect

## Slide 48
ACTIVITY 4 KNIGHT RIDER
Disconnect
Wire as per schematic
Hardware
Overview
☐ More LEDs
☐ Buttons (Pull-up config) & Debouncing
☐ Code “Knight Rider” effect
5 TIMES
PIN D13-D9

## Slide 49
ACTIVITY 4 KNIGHT RIDER
Push button
Hardware
Overview
☑ More LEDs
☐ Buttons (Pull-up config) & Debouncing
☐ Code “Knight Rider” effect
Always Connected
Connected when pressed

## Slide 50
TO GPIO
ACTIVITY 4 KNIGHT RIDER
Pull-up configuration
Default value is HIGH
Pressed value is LOW
Hardware
Always Connected
Connected when pressed
Overview
☑ More LEDs
☐ Buttons (Pull-up config) & Debouncing
☐ Code “Knight Rider” effect

## Slide 51
ACTIVITY 4 KNIGHT RIDER
Things are not perfect! ( ;_;)
Unwanted fluctuations (Aka noise)
Solution: add a capacitor to smoothen out noise
Hardware
Always Connected
Connected when pressed
Overview
☑ More LEDs
☐ Buttons (Pull-up config) & Debouncing
☐ Code “Knight Rider” effect

## Slide 52
ACTIVITY 4 KNIGHT RIDER
Wire as per Schematic
Hardware
2 TIMES
PIN D8 – D7
Always Connected
Connected when pressed
Overview
☑ More LEDs
☐ Buttons (Pull-up config) & Debouncing
☐ Code “Knight Rider” effect

## Slide 53
ACTIVITY 4 KNIGHT RIDER
Wiring Check
Hardware
Overview
☑ More LEDs
☐ Buttons (Pull-up config) & Debouncing
☐ Code “Knight Rider” effect

## Slide 54
ACTIVITY 4 KNIGHT RIDER
Try coding a knight rider effect (single direction)
Pseudocode:
Int delay_time (has max and min values)
setup:
led pins as output
pushbtn pins as input
main:
if push btn1 only: increment delay_time
if push btn2 only: decrement delay_time
turn LED 1 ON, wait delay_time, turn LED 1 OFF
…
turn LED 5 ON, wait delay_time, turn LED 5 OFF
Hardware
Overview
☑ More LEDs
☑ Buttons (Pull-up config) & Debouncing
☐ Code “Knight Rider” effect
Get input with `digitalRead(pin)`
5ms <= time <= 150ms
default value = 100ms
increment = 5ms
Notes: https://youtu.be/A362tbM6DVA?t=959

## Slide 55
ACTIVITY 4 KNIGHT RIDER
Something like this? Flash!
Hardware
Overview
☑ More LEDs
☑ Buttons (Pull-up config) & Debouncing
☐ Code “Knight Rider” effect
Notes: https://youtu.be/A362tbM6DVA?t=959

## Slide 56: ACTIVITY 4 KNIGHT RIDER
Task: Blink LEDs from left to right. Change speed with buttons.
Outcome
Hardware + Software familiarization
Input / Sensor
Recap
Input / Sensor are used to gather data from the world
Real life has “defects” compared to models
Hardware
Overview
☑ More LEDs
☑ Buttons (Pull-up config) & Debouncing
☑ Code “Knight Rider” effect

## Slide 57: QUESTIONS?

## Slide 58: DEMO 1 LED/SERVO CONTROLLER
Demo | Example Application
Battery (power bank) | Wildlife tracking, Autonomous robot
Remote control (ESP8266) | Smart TV, Robotic surgery, Marine exploration
E-paper screen | Name tag, Price tag, Bus stop ads

## Slide 59: DEMO 2 RASPBERRY PI
Raspbian on raspberry pi
Retro game arcade
Web server

## Slide 60: WHAT NEXT?
Buy your own?
Polling vs Interrupts
ESP8266? Zigbee? Bluetooth? WiFi?
IoT benefits and dangers
Slides, files, source code available:
https://github.com/MrTanoshii/Intro-Embedded-Systems

## Slide 61: QUESTIONS?

## Slide 62: THANK YOU
Tsen Chee Vincent LEUNG YIN KO
vincent.leungyinko@gmail.com
Slides, files, source code available:
https://github.com/MrTanoshii/Intro-Embedded-Systems